## Slide 1
EASYPILOT · 4AHITM DRONE PROJECT
The EasyPilot iOS App
A SwiftUI companion app that auto-discovers the drone on the network,
streams live telemetry at 10 Hz, flies a 3D simulator, and sends
flight commands over WebSocket.

## Slide 2
TECHNOLOGIES USED
The iOS stack
Swift 5
Apple's modern, type-safe language for the whole app.
SwiftUI
Declarative UI — TabView, glass cards, live bindings.
Network.framework
NWListener UDP discovery + WebSocket data link.
SceneKit
Real-time 3D flight simulator with .usdz drone model.
CoreMotion
Gyro / accelerometer read at 10 Hz for tilt control.
Espressif ESP32
On-drone firmware: WiFi, WebSocket server, beacon.

## Slide 3
CODE · SENSORS & COMMANDS
Phone tilt → drone command
// CoreMotion device-motion updates @ 10 Hz
motionManager.startDeviceMotionUpdates(to: .main) { data, _ in
let r = 180 / .pi
self.pitch = data.attitude.pitch * r
self.roll = data.attitude.roll * r
}
// Type-safe JSON command builder (ControlProfile)
func startBalanceCommand() -> String {
"""{"cmd":"START_BALANCE","baseThrottle":\(baseThrottle),
"kPRoll":\(kPRoll),"kPPitch":\(kPPitch)}"""
}

## Slide 4
CODE · THE THREADING CHALLENGE
Two threads, one drone
Physics on SceneKit's render thread must never touch SwiftUI directly — so internal state is kept separate from published state.
class DroneSimulator: ObservableObject {
// Main thread only — drives SwiftUI
@Published var simRoll = 0.0
@Published var isCrashed = false
// Render thread only — raw physics integration
var _roll = 0.0
var _vel: SIMD3<Float> = .zero
func tick(dt: Double) { /* render thread: physics */ }
func syncPublished() { /* main: _vars → @Published */ }
}

## Slide 5
WRAP-UP
Where we are & what's next
✓ Done
• Auto-discovery + WebSocket telemetry
• Live Dashboard with 3D drone view
• Full 3D flight Simulator (Rate / Balance / PosHold)
• Mode 2 virtual joysticks
• Tunable, savable control profiles
→ Next (Sprint 6)
• Live mode — fly the real drone from the joysticks
• Real MSP telemetry from the Betaflight FC
• Landscape UI polish & touch-aware stabilization
EasyPilot · 4AHITM HTL · iOS subsystem overview